# example_constant_flux_layer
  1. Purpose
Single surface-mounted cube in neutral open channel with a constant flux layer
  1. PALM-Version / SVN Revision
version 3.6, revision 250
  1. Required user code
none
  1. Input: example_constant_flux_layer_p3d
Cyclic lateral boundary conditions are used. The 3d-model is initialized with a linear vertical u-profile. Coriolis force is switched off (omega = 0.0). A direct external pressure gradient (dp_external = .T.) is applied in x-direction (dpdxy = -0.003, 0.0) that acts only above 80m (dp_level_b = 80.0). The vertical profile of the pressure gradient above 80m is sinusoidally smoothed (dp_smooth = .T.). The magnitude of the pressure gradient (0.003) has been determined empirically to ensure a time-averaged bulk velocity of approximately 1 m/s.
To set the open channel flow boundary condition, the vertical gradient of horizontal velocity components at the domain top is kept zero (bc_uv_t = 'neumann').
The cube is constructed using the generic topography case topography = 'single_building' with the default topography_grid_convention = 'cell_edge' (same as in case example_building).
  1. Preprocessing
none
  1. Program start - mrun call
mrun -d example_constant_flux_layer -h lcsgih -m 1500 -t 3600 -q testq -r 'd3# 3d# ts# pr#' -K parallel -X 8 -T 8 -n shared
  1. Monitoring: example_constant_flux_layer_rc
The 'run-control output' section is only valid for host lcsgih/lcsgib (HLRN-II in Hannover/Berlin). Other hosts may have slightly different timestep data.
  1. Postprocessing
none
  1. Miscellaneous
With sufficient spin-up time and averaging period, a layer of almost constant momentum flux can be observed between building_height = 40.0 and dp_level_b = 80.0.
  1. List of attachments
- example_constant_flux_layer_p3d
- example_constant_flux_layer_rc