# example_building
  1. Purpose
Single surface-mounted cube in neutral channel flow with constant bulk velocity
  1. PALM-Version / SVN Revision
version 4.0, revision 1541
  1. Required user code
none
  1. Input: example_building_p3d
Cyclic lateral boundary conditions are used. The 3d-model is initialized with constant vertical profiles. Coriolis force is switched off (omega = 0.0). A constant colume flow (i.e. constant bulk velocity) is maintained (conserve_volume_flow = .T.). The flow is explicitly set neutral (neutral = .T.), i.e. the prognostic equation for temperature and other buoyancy terms must not be calculated, which saves computation time. To set the channel flow boundary condition, the horizontal velocity components at the domain top are kept zero (bc_uv_t = 'dirichlet_0').
The cube is constructed using the generic topography case topography = 'single_building' with the default topography_grid_convention = 'cell_edge'.
  1. Preprocessing
none
  1. Program start - mrun call
mrun -d example_building -h lcmuk -m 1000 -t 3600 -r 'd3# 3d# ts# pr#' -K parallel -X 4 -T 4
  1. Monitoring: example_building_rc
The 'run-control output' section is only valid for host lcmuk (IMUK cluster). Other hosts may have slightly different timestep data.
  1. Postprocessing
none
  1. Miscellaneous
The results of the two cases example_building and example_topo_file should be same.
  1. List of attachments
- example_building_p3d
- example_building_rc