# example_dvr (This example only works for IMUK/HLRN!!)
  1. Purpose
Creating a 3D-animation with the dvr-software. The animation contains particles (with tails) and an isosurface of the liquid water content (ql).

A short guide how to use the dvr-software on IMUK/HLRN computers is given in the PALM-online-documentation in chapter 4.5.7.
  1. PALM-Version / SVN Revision
version 3.6, revision 338
  1. Required user code
none
  1. Input: example_dvr_p3d
inipar and d3par-parameters describe a convective boundary layer with zero mean wind and cyclic boundary conditions similar to example_cbl. Additionally, specific humidity is used and cloud physics is switched on. Particles (used for the animation) are controlled by the additional NAMELIST group &particles_par. The dvr-software is controlled by the NAMELIST group &dvrp_graphics_par.
  1. Preprocessing
none
  1. Program start - mrun call
mrun -d example_dvr -h lcsgih -K parallel -X16 -T4 -t 3600 -q testq -r 'd3#' -p dvrp_graphics
  1. Monitoring: example_dvr_rc
The 'run-control output' section is only valid for host lcsgih (HLRN-II in Hannover).
  1. Postprocessing
See chapter 4.5.7 of the online-documentation.
  1. Miscellaneous
Figure 1 shows a snapshot from the animation.
  1. List of attachments
- example_dvr_p3d
- example_dvr_rc

Figure 1

Snapshot from the end of the animation. Particle and tails colors show the deviation of temperature from the respective horizontal average (as a measure for buoyanvcy). The isosurface encloses areas with a liquid water content larger than 0.2 g/kg.