Coordinate variables:

(float) Dmid
geometric mean diameter of a aerosol size bin (in m)
attributes
(char) long_name	„geometric mean diameter of an aerosol	size bin“
(char) standard name	„aerosol_geometric_mean_diameter“
(char) units	„m“

(float) profile_z
height above ground of aerosol and gas input/background profile
data (e.g. from a larger scale model)
attributes
(char) long_name	„height above origin“
(char) standard name	„height_above_mean_sea_level”, must only
be set if “origin_z = 0”
(char) units	„m“
(char) axis	„Z“
(char) positive	„up“

Dimensions:

(integer)	composition_index	description: index of each chemical	component in salsa

Aerosol data [PIDS_SALSA]

[aerosol] aerosol_emission_values([Dmid],ncat,[dt_emission],[z],y,x)

description: Emission values of aerosol particles per size bin. The	coordinates vary based on the chosen level of detail.
type: NC_FLOAT
coordinates:
Dmid	geometric mean diameter of a aerosol size bin (in m)	(lod = 2 and lod = 3 only)
ncat	number of categories (this is needed to set the chemical
composition of aerosols)
dt_emission	time step (in s) (lod = 2 and 3?)
z	z-position (in m) (lod = 3 only)
y	y-position (in m)
x	x-position (in m)

attributes:
(integer)	lod	level of detail (1,2)
lod = 1	Emissions are provided in categories	and yearly as PM2.5. They are then	rescaled by pre-defined re-scaling	factors.
lod = 2	Emissions are provided for each	point in space and at given points in	time. Surface emission.
lod = 3	Emissions are provided for each	point in space (z,y,x) and at given	points in time. 3D-emission.
(char) long_name	"emission values"
(char) standard_name	"emission_values"
(float) dt_emission	e.g. "3600.0" (lod = 2 only)
(char) units	„kg/grid/yr“ (lod = 1) „kg/m2/dt_emission“ (lod = 2)	„#/m3/dt_emission“ (lod = 3)
(float) _FillValue	= -9999.0f
(char) coordinates	= „E_UTM N_UTM lon lat“
(char) grid_mapping	= „crsUTM: E_UTM N_UTM crsETRS: lon lat“

[aerosol] profile_mass_fracs_a/b(composition_index,z_profile)
description: Vertical profile of the mass fractions of background/initial
aerosol concentration: subrange a/b.
type: NC_FLOAT
coordinates:
composition_index	1: H2SO4 (sulphuric acid),
2: OC (organic carbon),
3: BC (black carbon),
4: DU (dust),
5: SS (sea salt),
6: HNO3 (nitric acid),
7: NH3 (ammonia)
z_profile	z-position (in m) of the initial/background	profile
attributes:
(char) long_name	"mass fraction profile: a/b bins"
(char) standard_name	"mass_fracs_a/b_profile"
(char) units	„“
(float) _FillValue	= -9999.0f

[aerosol] emission_mass_fracs(ncat,composition_index)

description: Mass fractions of aerosol emissions. The sum per each ncat	must be equal to one (lod = 2 only).
type: NC_FLOAT
coordinates:
ncat	number of categories
composition_index	1: H2SO4 (sulphuric acid),
2: OC (organic carbon),
3: BC (black carbon),
4: DU (dust),
5: SS (sea salt),
6: HNO3 (nitric acid),
7: NH3 (ammonia)

attributes:
(char) long_name	"mass fractions of aerosol emission"
(char) standard_name	"mass_fracs_emission"
(char) units	„“
(float) _FillValue	= -9999.0f

[aerosol] profile_nsect(Dmid,profile_z)

description: Vertical profile of aerosol particles per size bin at levels	profile_z.
type: NC_FLOAT
coordinates:
Dmid	geometric mean diameter of a aerosol size bin (in m)
profile_z	vertical levels of profile data (in m)
attributes:
(char) long_name	"vertical profile of aerosol size distribution"
(char) standard_name	"profile_nsect"
(char) units	„#/m3“
(float) _FillValue	= -9999.0f

Use these from the chemistry input: [PIDS_CHEM]

[chemistry] emission_category_index(ncat)

description: Category index of the emission quantity in question (e.g. 1	= traffic emissions)
type: NC_BYTE
coordinates:
ncat	number of categories

attributes:
(char) long_name	"emission category index"
(char) standard_name	"emission_cat_index"
(char) units	„“

[chemistry] emission_category_name(ncat)

description: Emission categories names (match to
emission_category_index of the same index element)
type: NC_STRING
coordinates:
ncat	number of categories

attributes:
(char) long_name	"emission category name"
(char) standard_name	"emission_cat_name"
(char) units	„“

[chemistry] emission_time_factors(ncat,[nhoursyear], [nmonthdayhour])

description: Emission time scaling factors for emission_values (lod = 1).	Two different time factors are possible: 1) Scaling according to	month‑day‑hour classification (lod = 1), or scaling for each hour	of the year (lod = 2).
type: NC_FLOAT
coordinates:
ncat	number of emission categories
nhoursyear	number of time scaling factors (lod = 2 only)
nmonthdayhour	number of time scaling factors (lod = 1 only)

attributes:
(integer)	lod	level of detail (1,2)
lod = 1	Classification in month-day-hour
lod = 2	Scaling factors for each hour of the year
(char) long_name	"emission time scaling factors"
(char) standard_name	"emission_time_scaling_factors"
(char) units	„“

[chemistry] emission_stack_height(y,x)

description: Height of the stacks
type: NC_FLOAT
coordinates:
y	y-position (in m)
x	x-position (in m)

attributes:
(char) long_name	"emission stack height"
(char) standard_name	"emission_stack_height"
(char) units	„m“
(float) _FillValue	= -9999.0f
(char) coordinates	„E_UTM N_UTM lon lat“
(char) grid_mapping	= „crsUTM: E_UTM N_UTM crsETRS: lon lat“

[chemistry] profile_H2SO4(profile_z)

description: Vertical profile of H2SO4 at levels profile_z.
type: NC_FLOAT
coordinates:
profile_z	vertical levels of profile data (in m)
attributes:
(char) long_name	"vertical profile of H2SO4"
(char) standard_name	"profile_H2SO4"
(char) units	„#/m3“
(float) _FillValue	= -9999.0f

[chemistry] profile_HNO3(profile_z)

description: Vertical profile of HNO3 at levels profile_z.
type: NC_FLOAT
coordinates:
profile_z	vertical levels of profile data (in m)
attributes:
(char) long_name	"vertical profile of HNO3"
(char) standard_name	"profile_HNO3"
(char) units	„#/m3“
(float) _FillValue	= -9999.0f

[chemistry] profile_NH3(profile_z)

description: Vertical profile of NH3 at levels profile_z.
type: NC_FLOAT
coordinates:
profile_z	vertical levels of profile data (in m)
attributes:
(char) long_name	"vertical profile of NH3"
(char) standard_name	"profile_NH3"
(char) units	„#/m3“
(float) _FillValue	= -9999.0f

[chemistry] profile_OCNV(profile_z)

description: Vertical profile of non-volatile organic gases at levels profile_z.
type: NC_FLOAT
coordinates:
profile_z	vertical levels of profile data (in m)
attributes:
(char) long_name	"vertical profile of OCNV"
(char) standard_name	"profile_OCNV"
(char) units	„#/m3“
(float) _FillValue	= -9999.0f

[chemistry] profile_OCSV(profile_z)

description: Vertical profile of OCSV at levels profile_z.
type: NC_FLOAT
coordinates:
profile_z	vertical levels of profile data (in m)
attributes:
(char) long_name	"vertical profile of OCSV"
(char) standard_name	"profile_OCSV"
(char) units	„#/m3“
(float) _FillValue	= -9999.0f