# example_building
  1. Purpose
Single surface-mounted cube in neutral channel flow with constant bulk velocity
  1. PALM-Version / SVN Revision
version 3.6, revision 244
  1. Required user code
none
  1. Input: example_building_p3d
Cyclic lateral boundary conditions are used. The 3d-model is initialized with constant vertical profiles. Coriolis force is switched off (omega = 0.0). A constant colume flow (i.e. constant bulk velocity) is maintained (conserve_volume_flow = .T.). To set the channel flow boundary condition, the horizontal velocity components at the domain top are kept zero (bc_uv_t = 'dirichlet_0').
The cube is constructed using the generic topography case topography = 'single_building' with the default topography_grid_convention = 'cell_edge'.
  1. Preprocessing
none
  1. Program start - mrun call
mrun -d example_building -h lcsgih -m 1500 -t 3600 -q testq -r 'd3# 3d# ts# pr#' -K parallel -X 2 -T 2 -n shared
  1. Monitoring: example_building_rc
The 'run-control output' section is only valid for host lcsgih/lcsgib (HLRN-II in Hannover/Berlin). Other hosts may have slightly different timestep data.
  1. Postprocessing
none
  1. Miscellaneous
The results of the two cases example_building and example_topo_file should be same.
  1. List of attachments
- example_building_p3d
- example_building_rc